## Slide 1: Strategic Development of Bioenergy in the Western States
Task 5: Cost Benefit Analysis
October 10, 2007
Gregg Morris, Future Resources Assoc., Inc.

## Slide 2: Task Overview
Objective
  Analyze the costs and benefits of producing liquid fuels from biomass resources in the West
Methodology
  Adapt benefits model to liquid fuels trajectories
  Load impacts data from tasks 1 – 4 and determine costs and benefits

## Slide 3: Overview of Benefits Model
Impacts
air pollution
greenhouse gases
landfill consumption
forest deterioration
watershed degradation
catastrophic wildfires
Alternative Fates
open burning
spreading/composting
forest accumulation
landfilling
Biomass Resources
mill residues
forest residues
agric. residues
urban residues
crops
Fossil Fuel
Use
Unit
Impacts
Fuel Use
energy production
OR
Alternative
Fate Factors
Net benefits = impacts of alt. fates + impacts of avoided fossil fuel use - impacts of biomass fuel production and use

## Slide 4: Alternative Fates for Feedstocks
Wastes and Residues
  Agricultural residues (field and processing)
  Forestry residues (mill, in-forest)
  Municipal residues
  Animal wastes
Crops
  Corn
  Oil seed crops
  Herbaceous energy crops

## Slide 5: Global Carbon Cycle
Biomass C
150 qmole
Atmospheric C
60 qmole
Fossil C
800 qmole
Fossil Fuels add New Carbon to the Active Cycle
Carbon stocks in the biosphere and atmosphere are linked and in rapid exchange.
Natural
Sequestration
8 qmole/yr
0.5 qmole/yr
0.25 qmole/yr
Primarily Dissolution in the Oceans

## Slide 6: Biomass and the Global Carbon Cycle
Biomass C
150 qmole
Atmospheric C
60 qmole
The transfers of carbon between the atmosphere and biomass can be out of balance, increasing or decreasing the amount of carbon in the atmosphere
Biomass C
Atmospheric CO2
rt = 120 yrs
Atm.CH4
rt = 12 yrs
CH4 is 25 times more potent as a ghg than CO2, although it has a shorter residence time.
OR
Net

## Slide 7: Summary of Key Results
Use of wastes and residues for energy production provides benefits by eliminating fossil fuel use, and by mitigating the impacts of conventional disposal practices
Crops provide net benefits from fuels conversion when they are produced in conjunction with higher-valued co-products, or when their production provides other environmental benefits, such as land remediation