## Slide 1: WGA TRANSPORTATION FUELS FOR THE FUTURE INITIATIVE Coal to Liquids Report Summary
Graham Parker
Transportation Fuels for the Future Workshop
Denver, CO
October 10-12, 2007

## Slide 2: Coal-to-Liquids (CTL) Background
Coal-based liquid fuels are indirectly produced by:
  gasifying pulverized coal to produce raw syngas.
  cleanup of the syngas stream to remove contaminants/CO2.
  production of liquid hydrocarbons via a Fischer-Tropsch (FT) catalytic process.
  product upgrading (hydrocracking) to produce the desired mix of fuels.
No full-scale commercial CTL operating plants in U.S.
  Most significant experience by Sasol, South Africa @~150,000 bbl/day.
  U.S. commercial plants are under design in WY, PA, IL, MS, & OH.
FT is a premium/stable fuel with ultra low sulfur & aromatics, high cetane, and high Btu content.
  Fuel markets include DoD (JP-8/marine diesel), states, refiners and blenders.
With ~65% of the U.S. coal resource, the West is well-positioned to supply a significant fraction of the country’s 30 million barrel/day oil consumption via a mature CTL industry.
Notes: Gayle is a huge proponent of biomass
<number>

## Slide 3: Summary Recommendations
Promote and establish alternative market-based incentive structures to help overcome the very high capital cost and associated financial risks with CTL plant construction.
Establish a trained/educated workforce for design/construction/operation of CTL plants.
Develop robust infrastructure (rail/pipeline/biomass transport/CO2 storage) as well as permitting, siting and regulatory/oversight environment to foster CTL industry.
Undertake RD&D including full-scale demonstration of coal/biomass co-processing.
Establish regulatory framework for CO2 management & pursue carbon capture and storage (CCS) projects.
Notes: <number>

## Slide 4: Status and Schedule of CTL Report
Advisory Committee guidance on path forward for current Draft Report and recommendations provided to CTL work group on 09/07.
Final Draft Report and recommendations to CTL work group on 09/28.
CTL work group review and comments on Final Draft Report due 10/15.
Draft Final report to Advisory Committee and for public comment 10/18.
Comments due on Draft Final Report on 10/22.
Final Report to Advisory Committee on 10/24.