## Slide 1: Improving the Characterization Program for Contact-Handled Transuranic Waste Bound for the Waste Isolation Pilot Plant
The National Research Council
January 15, 2003

## Slide 2: Statement of Task
The objectives of this study were to:
  provide a review of the Department of Energy’s program for characterization and characterization-related transportation issues for transuranic waste; and
  recommend improvements to increase the program’s technical soundness, efficiency, cost-effectiveness, and safety to workers and the public.
The study will address programmatic, policy, and societal impacts of changes in characterization requirements.
The study will not address requirements for the characterization of remote-handled transuranic waste or non-technical transportation requirements.

## Slide 3: Committee on optimizing the characterization and transportation of transuranic waste destined for the Waste Isolation Pilot Plant
12 committee members were chosen for their expertise in:
  Actinide/physical chemistry
  Hazardous and radioactive waste management regulations
  Health physics
  History of characterization program at WIPP
  Public policy/Social sciences
  Radioactive waste transportation regulations
  Risk/benefit assessment
  Technical aspects of waste characterization
9 experts under the supervision of an independent review monitor conducted a review of the report
Responsibility for final content rests with the authoring committee and the National Research Council

## Slide 4: Observations
That WIPP is open and operating is a significant achievement
  DOE is making a significant contribution to the clean up of the weapons complex
  DOE’s radiation protection program is successful
WIPP has followed a regulatory path typical of many first-of-a-kind facilities:
  Initial conservative approach to meeting laws and regulations
  Modification of regulatory documents based on better understanding gained through operational experience and analyses

## Slide 5: Bottom Line
After four years of WIPP operations, changes to the characterization program are expected and are part of the normal learning process for a first-of-a-kind facility
A regulatory process exists under which changes can be made to the waste characterization program
A structured and quantitative analysis is needed to support requests for changes to the regulator and to communicate with the public

## Slide 6: Findings and Recommendations
The committee first recommends a structured and quantitative analysis of the value of characterization activities on which DOE can base decisions about changes and improve communication.
  Committee provides 3 illustrative examples of a structured and quantitative analysis to support the proposed changes
The committee provides 5 additional recommendations for improving operations whatever activities are conducted.

## Slide 7
Finding 1: DOE has not presented a systematic analysis to support potential changes to the regulators or to the public. Although DOE has performed analyses of many aspects of operations related to WIPP performance, including transportation, the committee could find no studies that explicitly, systematically, and quantitatively link its waste characterization program to risks to the public, workers, or the environment.
Recommendation 1: DOE should use a systematic and quantitative approach to determine the value of the information currently obtained by its waste characterization activities and the impact of changes to them. This approach should also be used to support permit modification requests and communicate with the public.

## Slide 8: Finding and Recommendation 1 (cont.)
Three characterization activities appear to be candidates for the complete application of the analytical framework proposed by the committee:
  headspace gas sampling and analysis,
  homogeneous waste sampling and analysis, and
  visual examination to confirm radiography results

## Slide 9: A structured and quantitative analytical framework
?
Revised Characterization Activity/Program
Regulator’s
Decision
Stakeholder
Input
Experience and Analysis-Based Learning
Information Generated by Characterization
Decisions based on Information
Risks, Costs, and
Other Impacts
Permit Modification
Request
Current Characterization Activity/Program

## Slide 10
Finding 2: DOE now has four years of operational experience with the National Transuranic Waste Management program that can be used to improve waste characterization activities.
Recommendation 2: DOE should use its increasing experience base and advances in technology to improve the current transuranic waste characterization program.

## Slide 11
Finding 3: Current characterization activities are applied generically to all waste types and, with few exceptions, are not tailored to particular waste streams.
Recommendation 3: DOE should propose to its regulators a more flexible waste characterization program that can take into account the properties of different waste streams, allowing more efficient and effective waste characterization operations.

## Slide 12
Finding 4: DOE is currently using only one of the four methods approved by EPA to qualify information as Acceptable Knowledge, namely, confirmation by measurement. Use of the other methods could reduce waste handling and costs, increase the efficiency of characterization activities, and extend the use of Acceptable Knowledge for waste generated in the future.
Recommendation 4: DOE should request authorization from its regulators to use all four methods allowed by EPA for qualifying waste information to be used as Acceptable Knowledge.

## Slide 13
Finding 5: Transportation agreements for WIPP shipments have been fashioned over many years of negotiation between DOE and the corridor states. Any changes in the WIPP characterization program could be viewed as undermining these institutional agreements.
Recommendation 5: In addition to working with its regulators, DOE should ensure that corridor states are kept informed of negotiations for changes to the characterization program. Specifically, DOE should communicate effectively with the Western Governors Association, the Southern States Energy Board, and similar groups representing corridor states. DOE should analyze, publish, and present to corridor states’ representatives any impact of proposed changes on transportation safety.

## Slide 14
Finding 6: Stakeholders have many concerns about WIPP program-related operations.
Recommendation 6: DOE should publish clearly written analyses of proposed changes to the characterization program to document that these changes do not adversely affect the protection of worker and public health and/or of the environment. DOE should also provide public access to information about WIPP and its operations, including the WIPP Waste Information System, and communicate interactively with state officials, tribes, public interest groups, and scientific oversight organizations. The proposed analytical framework could provide a technically defensible approach for supporting changes to the characterization program.